## Slide 1: Tutorial on OpenFlow Fed4FIRE – Open Tutorial Day
Carlos Bermudo (carlos.bermudo@i2cat.net)
Berlin, December 10th 2014

## Slide 2: Introduction
Refreshing OF slicing
OpenFlow testbeds in Fed4FIRE
Running an OF experiment
  Create an OF topology including i2CAT and VWall VMs and run an OF controller (emulating L2 learning switch) that controls the switch in the topology.
POX tricks & tips

## Slide 3: Definition: OpenFlow
Characteristics:
  Software controller
  Secure channel with devices
  Matching on OF packet headers

## Slide 4: Software: OpenFlow controllers’ overview
Platform / Framework that allow experimenters to develop components / applications to control the behavior of their data flows
NOX, POX
  NOX: 1st OpenFlow controller
  POX: high-level SDN API
  Supported protocol(s): OpenFlow 1.0
  Supported language(s): C++ (NOX), Python (POX)
  https://github.com/noxrepo/nox-classic/wiki/Developing-in-NOX
  https://openflow.stanford.edu/display/ONL/POX+Wiki
Ryu
  Open-sourced Network Operating System (NOS)
  Supported protocol(s): OpenFlow 1.0, 1.3, 1.4
  Supported language(s): Python
  http://ryu.readthedocs.org/en/latest/writing_ryu_app.html
http://yuba.stanford.edu/~casado/of-sw.html

## Slide 5: Software: Flow slicing
The problem
  Each experiment generates a set of data flows
  Multiple experiments running at the same time
  Different data flows (experiments) must be isolated
FlowVisor
  Special purpose OpenFlow controller that acts as a transparent proxy between OpenFlow switches and multiple OpenFlow (user) controllers.

## Slide 6: Software: Flow slicing
FlowVisor

## Slide 7: OpenFlow testbeds: UNIVBRIS
4 x Packet Switches (NEC IP8800)
2 x dedicated virtualization servers
3 x fixed WDM optical switches (ADVA FSP3000)

## Slide 8: OpenFlow testbeds: i2CAT
5 x NEC IP8800/S3640-24T2XW, 24 ports (1/10GE)
3 x dedicated physical servers

## Slide 9: OF testbeds in federation environments
Connectivity in Fed4FIRE
UNIVBRIS
i2CAT
Public Internet
VirtualWall
L2 VPN

## Slide 10: Running an experiment
Creating the slivers
VT AM
OF AM
SFA
SFA
FV
CLI/UI
jFed
SFI
OMNI
createSliver
createSliver
createSliver
create vm
define links
create vm
create vm

## Slide 11: Running an experiment
Creating the slivers
Setting the controller
VT AM
OF AM
SFA
SFA
FV
CLI/UI
jFed
SFI
OMNI
set controller

## Slide 12: Running an experiment
Creating the slivers
Setting the controller
Sending data within the slice
VT AM
OF AM
SFA
SFA
FV
CLI/UI
jFed
SFI
OMNI
transmitter
receiver

## Slide 13: Let’s Create a Slice
Create the VWall Node using jFed
Create the i2CAT VMs
Reserve FS at i2CAT

## Slide 14: Supporting files
Download and unzip the file from:
  https://github.com/fp7-ofelia/ocf/wiki/GENI-usage
    vtam_request_i2cat
    ofam_request_i2cat
    jFedi2CAT
Let’s take a look at the topology
Verdaguer
TutorialVM1
TutorialCtrl
Rodoreda
TutorialVM2
eth1
eth1
eth1
12
12
1
3
00:10:00:00:00:00:00:03
00:10:00:00:00:00:00:01
VirtualWall
node
13 (vlan 186)
14 (vlan 190)
15 (vlan 197)

## Slide 15: VT AM Request
<?xml version="1.0"?>
<RSpec type="SFA" expires="2015-02-18T11:21:29Z" generated="2013-02-18T10:21:29Z">
<network name="vt_ocf" slice="">
<node component_manager_id="urn:publicid:IDN+i2cat:vtam+cm" component_id="urn:publicid:IDN+i2cat:vtam+node+Verdaguer" exclusive="false" component_name="urn:publicid:IDN+i2cat:vtam+node+Verdaguer">
<sliver>
<name>tutorialVM1</name>
<uuid>myuuid</uuid>
<project-id>project4</project-id>
<slice-id>slice2</slice-id>
<slice-name>slice2</slice-name>
<operating-system-type>GNU/Linux</operating-system-type>
<operating-system-version>5.0</operating-system-version>
<operating-system-distribution>Debian</operating-system-distribution>
<server-id>serverid</server-id>
<hd-setup-type>file-image</hd-setup-type>
<hd-origin-path>default/test/lenny</hd-origin-path>
<virtualization-setup-type>paravirtualization</virtualization-setup-type>
<memory-mb>128</memory-mb>
</sliver>
</node>
<node component_manager_id="urn:publicid:IDN+i2cat:vtam+cm" component_id="urn:publicid:IDN+i2cat:vtam+node+Verdaguer" exclusive="false" component_name="urn:publicid:IDN+i2cat:vtam+node+Verdaguer">
<name>tutorialVMCtrl</name> …
</node>
<node component_manager_id="urn:publicid:IDN+i2cat:vtam+cm" component_id="urn:publicid:IDN+i2cat:vtam+node+Rodoreda" exclusive="false" component_name="urn:publicid:IDN+i2cat:vtam+node+Rodoreda">
<name>tutorialVM2</name> ….
</node>
</network>
</RSpec>

## Slide 16: OF AM Request
<rspec xmlns="https://github.com/fp7-ofelia/ocf/blob/ocf.rspecs/openflow/schemas/request.xsd" […] type="request">
<openflow:sliver email="a@b.com" description="OF request example">
<openflow:controller url="tcp:10.216.12.57:6633" type="primary"/>
<openflow:group name="fs1">
<openflow:datapath component_id="urn:publicid:IDN+openflow:optin:i2cat.of_ocf+datapath:00:10:00:00:00:00:00:01"
component_manager_id="urn:publicid:IDN+openflow:optin:i2cat.of_optin+authority+am"
dpid="00:10:00:00:00:00:00:01">
<openflow:port name="GBE0/4" num="3"/>
<openflow:port name="GBE0/12" num="12"/>
</openflow:datapath>
<openflow:datapath component_id="urn:publicid:IDN+openflow:optin:i2cat.of_ocf+datapath:00:10:00:00:00:00:00:03"
component_manager_id="urn:publicid:IDN+openflow:optin:i2cat.of_optin+authority+am"
dpid="00:10:00:00:00:00:00:03">
<openflow:port name="GBE0/3" num="1"/>
<openflow:port name="GBE0/3" num="12"/>
<openflow:port name="GBE0/13" num="13"/>
</openflow:datapath>
</openflow:group>
<openflow:match>
<openflow:use-group name="fs1" />
<openflow:packet>
<openflow:dl_vlan value=“186" />
</openflow:packet>
</openflow:match>
</openflow:sliver>
</rspec>

## Slide 17: Creating a Node on vwall2 using jFed
http://jfed.iminds.be
Quick Start
Login
Open
  jFedi2CAT.rspec
Run

## Slide 18: Creating VM at i2CAT
Edit file i2catVM.rspec
  <name>tutorialVM</name>  alphanumeric name for the virtual machine
Execute
  omni createslice <SLICENAME>
  omni -a https://137.222.204.27:5001/xmlrpc/sfa/ createsliver <SLICENAME> vtam_request_i2cat.rspec
Save the returned IP address, it will be the controller

## Slide 19: Reserving the FS at i2CAT
Edit i2catOF.rspec
  <openflow:controller url="tcp:10.216.12.XX:6633" type="primary"/>  replace controller IP by the previous one returned by i2CAT manifest RSpec
  <openflow:dl_vlan value=“YYY" />  vlan number depends on port selected to link with VWall
Execute
  omni -a https://137.222.204.27:5005/xmlrpc/sfa/ createsliver <SLICENAME> ofam_request_i2cat.rspec
Switch 3 |  | Switch 4 | 
Port | Vlan | Port | Vlan
13 | 186 | 13 | 187
14 | 190 | 14 | 188
15 | 197 | 15 | 189

## Slide 20: Access & Configure the OFELIA VMs
Open console in vwall node
ssh the VMs using root@vm_ip
apt-get install vlan
ifconfig <iface> up
  for this tutorial: eth1, depending on IFs between servers and switchs
vconfig add <iface> <vlan>
  VLANs shared with VWall 186-190 and 197
ifconfig <iface>.<vlan> 192.168.12.X/24 up

## Slide 21: Access & Configure the OFELIA VMs
Open console in vwall node
sudo vconfig add vlan1001 <vlan>
  Vlan1001 is the IF linked to i2CAT
  Command will create IF vlanX
  VLANs shared with i2CAT 186-190 and 197
ifconfig <iface> 192.168.12.X/24 up

## Slide 22: Access and configure the Controller
access to the vwall node
ssh to the controller (root:openflow)
apt-get update
apt-get install git
git clone https://github.com/noxrepo/pox.git
cd pox/
git checkout dart  Otherwise won’t work
./pox.py log.level --CRITICAL forwarding.l2_learning

## Slide 23: Try ping between nodes
Ping, ping, ping
  from i2CAT VM to i2CAT VM
  from Virtual Wall to i2CAT VM and viceversa
POX overview
To run an app:
./pox.py <python path to app name>
  port
  verbose
  loglevel

## Slide 24: POX overview
To run an app:
./pox.py <python path to app name>
  --port
  --verbose
  --loglevel

## Slide 25: Useful links
POX Tutorial
  http://sdnhub.org/tutorials/pox/
POX Wiki
  https://openflow.stanford.edu/display/ONL/POX+Wiki#POXWiki-FAQs
OpenFlow Tutorial with POX
  http://blog.pythonicneteng.com/2013/02/openflow-tutorial-with-pox.html
UnivBris user manual
  http://univbrisofeliaf4f.blogs.ilrt.org/

## Slide 26: Questions?
OpenFlow SWITCH
CONTROLLER
carlos.bermudo@i2cat.net

## Slide 27: Acknowledgement
This work was carried out with the support of the Fed4FIRE-project (“Federation for FIRE"), an Integrated project receiving funding from the European Union’s Seventh Framework Programme for research, technological development and demonstration under grant agreement no 318389
It does not necessarily reflect the views of the European Commission. The European Commission is not liable for any use that may be made of the information contained herein.
Notes: THIS SLIDE SHOULD ALWAYS BE THE LAST SLIDE OF YOUR PRESENTATION!!!!

## Slide 28: Backup slides

## Slide 29: My first App
In /pox directory, create a *.py file
Import (at least) nox core and OF lib and some utils
  from pox.core import core
  import pox.openflow.libopenflow_01 as of
  from pox.lib.util import dpid_to_str
Set up the launch() method
Develop your app
def launch (**kwargs):
core.registerNew(<MyApp>,kwargs)

## Slide 30: POX tricks – Listen events
Register callback functions for specific events thrown by either the OpenFlow handler module or specific modules like Topology Discovery
  From the launch or from the init of a class, perform core.openflow.addListenerByName(“EVENTNAME”, CALLBACK_FUNC, PRIORITY)
Register object with the OpenFlow handler module or specific modules like Topology Discovery
  From typically the init of a class, perform addListeners(self). Once this is added, the controller will look for a function with the name _handle_EVENTNAME(self, event). This method is automatically registered as an event handler.
[1]
[1]

## Slide 31: POX tricks – Parse packets
From a handled event (i. e. packet-in) POX provides ways to parse the packet and identify the headers.
packet = event.parsed
mac = packet.src
packet.type [ipv4, icpm, tcp, etc.]

## Slide 32: POX tricks – Send messages
msg = of.ofp_packet_out()
message msg.buffer_id = event.ofp.buffer_id msg.in_port = packet_in.in_port
msg.match = of.ofp_match.from_packet(packet)
action = of.ofp_action_output(port = of.OFPP_FLOOD)
msg.actions.append(action)
self.connection.send(msg) [1]

## Slide 33: Advices
Read ALL samples
Catch ALL exceptions
Log ALL with info
Use existing apps
Remember that POX can load several apps at the same time
If possible, apply TDD. Ensure that the code of your app is almost bullet-proof
Slide powered by master Yoda

## Slide 34: UnivBris OF AM Request
<?xml version="1.0" encoding="UTF-8"?>
<rspec xmlns="http://www.geni.net/resources/rspec/3"
xmlns:xs="http://www.w3.org/2001/XMLSchema-instance"
xmlns:openflow="/opt/ofelia/ofam/local/schemas"
xs:schemaLocation="http://www.geni.net/resources/rspec/3
http://www.geni.net/resources/rspec/3/request.xsd
http://www.geni.net/resources/rspec/ext/openflow/3
http://www.geni.net/resources/rspec/ext/openflow/3/of-resv.xsd"
type="request">
<openflow:sliver email="carlos.bermudo@i2cat.net" description="From UOB delphi to i2cat VPN">
<openflow:controller url="tcp:10.216.12.29:6633" type="primary"/>
<openflow:group name="fs1">
<openflow:datapath component_manager_id="urn:publicid:IDN+openflow:ofam:univbris+authority+cm"
component_id="urn:publicid:IDN+openflow:ofam:univbris+datapath+05:00:00:00:00:00:00:01"
dpid="05:00:00:00:00:00:00:01">
<openflow:port name="GBE0/6" num="6"/>
<openflow:port name="GBE0/5" num="5"/>
</openflow:datapath>
<openflow:datapath component_id="urn:publicid:IDN+openflow:ofam:univbris+datapath+05:00:00:00:00:00:00:03"
component_manager_id="urn:publicid:IDN+openflow:ofam:univbris+authority+cm"
dpid="05:00:00:00:00:00:00:03">
<openflow:port name="GBE0/19" num="18"/>
<openflow:port name="GBE0/7" num="7"/>
</openflow:datapath>
</openflow:group>
<openflow:match>
<openflow:use-group name="fs1" />
<openflow:packet>
<openflow:dl_vlan value= "778"/>
</openflow:packet>
</openflow:match>
</openflow:sliver>
</rspec>

## Slide 35: UnivBris VT AM Request
<RSpec type="SFA" expires="2014-06-13T11:21:29Z" generated="2014-06-13T10:21:29Z">
<network name="vt_ocf" slice="">
<node component_id="urn:publicid:IDN+univbris:vtam+node+cseedelphi" component_manager_id="urn:publicid:IDN+univbris:vtam+cm" component_name="urn:publicid:IDN+univbris:vtam+node+cseedelphi" exclusive="false">
<sliver>
<name>tutorialVM</name>
<uuid>myuuid</uuid>
<project-id>project1</project-id>
<slice-id>test8</slice-id>
<slice-name>test9</slice-name>
<operating-system-type>GNU/Linux</operating-system-type>
<operating-system-version>7.0</operating-system-version>
<operating-system-distribution>Debian</operating-system-distribution>
<server-id>serverid</server-id>
<hd-setup-type>full-file-image</hd-setup-type>
<hd-origin-path>debian7uob/debian7uob.img</hd-origin-path>
<virtualization-setup-type>hvm</virtualization-setup-type>
<memory-mb>1024</memory-mb>
<interfaces>
<interface ismgmt="true">
<name>eth0</name>
<mac>00:16:3E:2D:AE:27</mac>
<ip>10.216.22.60</ip>
<mask>255.255.255.0</mask>
<gw>10.216.20.1</gw>
<dns1>8.8.8.8</dns1>
<dns2>4.2.2.1</dns2>
</interface>
</interfaces>
</sliver>
</node>
</network>
</RSpec>

## Slide 36: Request Resources from VTAM (GeniV3)
  Allocate it First!
    omni -a https://137.222.204.27:5001/xmlrpc/geni/3/ -V3 allocate <SLICENAME> vtam_geni3_request_i2cat.rspec
  Provision it!
    omni -a https://137.222.204.27:5001/xmlrpc/geni/3/ -V3 provision <SLICENAME>
  RSpec:
  <?xml version="1.0" encoding="UTF-8" standalone="yes"?>
  <rspec generated="2014-03-22T01:53:21.460+01:00" type="request“ xsi:schemaLocation="http://www.geni.net/resources/rspec/3 http://www.geni.net/resources/rspec/3/request.xsd" xmlns="http://www.geni.net/resources/rspec/3" " " xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance">
  <node client_id="Verdaguer" component_id="urn:publicid:IDN+ocf:i2cat:vtam+node+Verdaguer" component_manager_id="urn:publicid:IDN+ocf:i2cat:vtam+authority+cm" exclusive="true">
  </node>
  </rspec>

## Slide 37: Requesting OFAM Resources (GeniV3)
  Allocate it First!
    omni -a https://137.222.204.27:5005/xmlrpc/geni/3/ -V3 allocate <SLICENAME> ofam_request_i2cat.rspec
  Provision it!
    omni -a https://137.222.204.27:5005/xmlrpc/geni/3/ -V3 provision <SLICENAME>
  Then wait for approval 